## Slide 1: Multiple Cars Tracking Basing on Kalman Filter
Team #13
Pengluo Wang; Kaiyu Zhang;
Shihao Luo
ECE 251B –Digital Signal Processing Ⅱ

## Slide 2: Contents
01
02
03
04
Problem
Data
Solutions
Results

## Slide 3: Problem
Background
  The automatic driving is one of the most important technical achievement, which still needs more promotion.
  Implement a set of algorithm to combine car detection and tracking together, to provide convenience for car driving.
What we did
  Use different methods implement the car detecting and tracking, and add boxes marking the multiple cars in the video.
  We choose Tensorflow Object Detection API for car detection.
  After getting the location information of detected cars, we make prediction using Kalman filter, and combine the prediction & measurement values as the real tracking value, to finish whole algorithm.

## Slide 4: Dataset
Video data
  The data we use is a set of video taken by the dashcam in front of our car, which is real and reliable.
  The data was taken in our daily life, including different situations: no cars, one car, more than one cars in the visual area.
  The cars in the video have several typical behaviors including intersection and overtaking.
(a)
(b)
(c)

## Slide 5: Method Introduction – Detection
Tensorflow object detection API
  An open source framework built on top of TensorFlow that makes it easy to construct, train and deploy object detection models.
  To use this build-in model, we applies SSD with MobileNet, a Single-Shot-Detection with MobileNet architecture trained on COCO dataset.
Single-Shot-Detection (SSD)
  SSD algorithm is an object detection algorithm that directly predicts the coordinates and categories of the objection with bounding box.
  SSD is much faster than those traditional detection models without losing the accuracy, by adding several separate prediction filters.
SSD advantages
  High Speed
  High Accuracy
  Can be applied with low resolution and video data
Notes: SSD model is based on a feed-forward convolutional network that produces a fixed-size collection of bounding boxes and scores for the presence of object class instances in those boxes, followed by a non-maximum suppression step to produce the final detections.

## Slide 6: Method Introduction – Detection
SSD – basic frames
  Using a small convolutional filter to predict object categories and offsets in bounding box locations.
  Using separate predictors (filters) for different aspect ratio detections.
  Applying these filters to multiple feature maps from the later stages of a network in order to perform detection at multiple scales.
  Train the data with ground truth boxes, and the obtained model can be used for detection.
Notes: SSD model is based on a feed-forward convolutional network that produces a fixed-size collection of bounding boxes and scores for the presence of object class instances in those boxes, followed by a non-maximum suppression step to produce the final detections.

## Slide 7: Method Introduction – Detection
SSD – outcome
  This model has been trained with COCO dataset, which can detect the following objects related to transportation:
Label | Objection
1 | Person
2 | Bicycle
3 | Car
4 | Motorcycle
5 | Bus
6 | Train
7 | Traffic Light
8 | Stop Sign

## Slide 8: Method Introduction – Detection
Flow chart
Notes: SSD model is based on a feed-forward convolutional network that produces a fixed-size collection of bounding boxes and scores for the presence of object class instances in those boxes, followed by a non-maximum suppression step to produce the final detections.

## Slide 9: Method Introduction – Detection
SSD – outcome
  Using a test image, we have the following outcome:

## Slide 10: Method Introduction – Tracking
Kalman filter
  An adaptive filter, with following important benefit features:
    Predict of object's future location;
    Correction of the prediction based on new measurements;
    Reduction of noise introduced by inaccurate detections;
    Facilitating the process of association of multiple objects to their tracks.
  Update process
    Prediction: uses previous states to predict the current state.
    Correction: uses the current measurement, such as detection bounding box location, to correct the state.

## Slide 11: Method Introduction – Tracking
Prediction
  Notations
    x: process state
    P: estimate error(noise) covariance
    A: state transition matrix
    Q: process noise covariance
    w: process noise,
  Equations
Correction
  Notations
    H: measurement function (matrix)
    z: measurement state
    R: measurement noise covariance
    K: Kalman gain
    v: measurement noise,
  Equations

## Slide 12: Method Introduction – Tracking
Kalman filter implementation – initialization
  Suppose current state
  Write into Matrix Form as update function, where
  is the state transition matrix
  In the project, dimension of is , since there are four locations to be tracked, which is left, down, right and up, representing the four corners of the bounding box.

## Slide 13: Method Introduction – Tracking
Kalman filter implementation – initialization
  Initial the measurement transition matrix , given that the detector only outputs the coordinate (not velocity and acceleration)
  Initialize noise covariance , :
    Initial , randomly.
    The value of shows the confidence of the confidence of prediction
Notes: A low R_ratio indicates a more reliable measurement.

## Slide 14: Intersection-over-Union（IoU）
IoU
  A parameter shows the accuracy of detection and prediction.
  Can be understood as the accuracy rate for each image
  For example:
Notes: SSD model is based on a feed-forward convolutional network that produces a fixed-size collection of bounding boxes and scores for the presence of object class instances in those boxes, followed by a non-maximum suppression step to produce the final detections.

## Slide 15
Linear-Assignment
  One of the fundamental combinatorial optimization in order to find a maximum weight matching (or minimum weight perfect matching) in a weighted bipartite graph.
  Implemented by package sklearn in Python.
  Produce the max matching between detection and tracking box in our project. The results are stored in list matched, unmatched_detections, and unmatched_trackers.
Detection-to-Tracker Assignment
 | D1 | D2 | D3 | D4
T1 | 0 | 0 | 1 | 0
T2 | 1 | 0 | 0 | 0
T3 | 0 | 0 | 0 | 0
IoU matrix
Notes: SSD model is based on a feed-forward convolutional network that produces a fixed-size collection of bounding boxes and scores for the presence of object class instances in those boxes, followed by a non-maximum suppression step to produce the final detections.

## Slide 16
Sequential processing
  Process each frame of the input video, implemented by package MoviePy.
  Deals with matched, unmatched_detections, and unmatched_trackers ob-tained from linear assignment of the IoU matrix for each frame.
False alarm & missed detection
  Introduce two important parameters, min_hits and max_losses: min_hits stands for the minimum number of consecutive matches to establish a tracker; max_loss stands for the maximum number of consecutive losses to delete a current track.
  Introduce a variable to discriminate false alarm and real target, a tracker is called good tracker if it has reached min_hits.
Pipeline
Notes: SSD model is based on a feed-forward convolutional network that produces a fixed-size collection of bounding boxes and scores for the presence of object class instances in those boxes, followed by a non-maximum suppression step to produce the final detections.

## Slide 17: Pipeline Diagram

## Slide 18: Results – Frame

## Slide 19: Results – Frame

## Slide 20: Results – Frame

## Slide 21: Results – Frame

## Slide 22: Results – Frame

## Slide 23: Results – Frame

## Slide 24: Results – Frame

## Slide 25: Results – Frame

## Slide 26: Results – Frame

## Slide 27: Results – Video

## Slide 28: Reference
[1]. Greg Welch, and Gary Bishop, An Introduction to the Kalman Filter, [University of North Carolina at Chapel Hill Chapel Hill], NC 27599-3175, July 24,2016
[2]. Wei Liu, Dragomir Anguelov, Dumitru Erhan, and Christian Szegedy, SSD: Single Shot MultiBox Detector, [cv.CS], Dec 29, 2016
[3]. Jonathan Huang, Vivek Rathod, Chen Sun, et al, Speed/accuracy trade-offs for modern convolutional object detectors, [cv.CS], Nov 30, 2016

## Slide 29
Thank You!
Q & A